## Slide 1: Hop or not to hop.

## Slide 2: Scenario
Get runner’s pulse
Talk directly when possible
Use relays to extent track coverage
  Simple relay
  RSSI relay

## Slide 3: Base Station RSSI Log plots dBm
Environment: Interference free clean AIR
Ptx = 0dBm “1mW”
Isotropic Antenna
  2.407GHz “ch1”
  Lambda = v/f
  2.7cm
  d0=0.01167
-84dBm at 159.3m
  Euclidian distance
  -94dBm from datasheet

## Slide 4: 0dBm vs -24dBm & Air vs Building
Change in transmit power
0dBm_AIR Track “159.3m”
  L400m, H=80m
-24dBm_AIR Track “10.1m”
  L30m, H=6m
  Reduced to 7.5% range
0dBm_Building Track “64.5m”
  L30m, H=6m
  Reduced to 32.25% range
-24dBm_Building Track “13.1cm”
  L20cm, H=4m
  Reduced to 0.035% range

## Slide 5: RSSI Fading
Reflection “Fast Fading”
  2.4GHz => Lambda = 12.5cm
  Destructive interference “Busty Errors”
  -60dBm to -70dBm
  In the range of tens to hundreds of milliseconds
  Simulated as 250ms occurrences
Diffraction and Scattering “Slow Fading”
  Shadowing effect “obstacles in the environment”
    Photographer at the finish line
    Toolshed
  In the range of tens of seconds to minutes
  Simulated as 13 seconds occurrences
Doppler fading “Changing signal behavior”
  Frequency shift due to movement of nodes
  Positive shift at run towards the base station
  2MHz wide channels
  One package length doppler shift running at 12kph
  Top of the track: 26.773Hz shift
  End of track: 29.698Hz shift
  Running at 50000kph = 1.1MHz shift

## Slide 6: Package Fading
1 lab at the track
  -84dBm threshold level
  480 packages (4/sec)
  Level crossing rate at 0.2
Marathon
  47 labs
  1087 Packages
IN RANGE direct or relayed package for half a track

## Slide 7: Lifetime Calculations
Battery End of Lifetime = Half Capacity
Max and min power transmission
  0dBm
  -24dBm
Sleep between packages or not
  4 packages = 0.0521s
    Transmit
    Receiving
    latency
Overshoot
  40% extra power usage at peak
  50milli seconds
POWER TABLE |  |  |  | 
Scenario | Transmission Power | Sleep | Overshoot after wake-up | Base Station Lifetime before half battery capacity (Hours)
1 | Max (0dBm) | No | No | 176,48
2 | Min (-24dBm) | No | No | 176,52
3 | Max (0dBm) | Yes | No | 13101,00
4 | Min (-24dBm) | Yes | No | 13319,00
5 | Max (0dBm) | Yes | Yes | 796,32
6 | Min (-24dBm) | Yes | Yes | 797,11
Radio Off
Radio On
Overshoot

## Slide 8: Receive/Transmit Power
“Idle” Receiving
  18,0 mA
Transmit with 0,0 dB
  8,0 mA
Transmit with -12,5 dB
  13,0 mA
Transmit with -25,0 dB
  17,5 mA
”Idle” Receiving
Transmit with 0,0 dB
Transmit with -25,0 dB
Transmit with -12,5 dB

## Slide 9: Results
Best to hop when
  Out of range
  RSSI -40
  Deep fading
The antenna is expensive battery wise.

## Slide 10: ToHopOrNot
Will the next package be bad?
  Signal strength
  Distance
  Received or not package
Multi linear regression
  Isotropic Antenna
  Binary fading behavior
  Modeled as a random variable at any distance
Could be fun to do a real-life experiment!